## Slide 1: System Types
Continuous
  Variables take on continuous values
  Described by ordinary differential equations (Example: mass/energy flow systems)
Discrete
  Variables take on discrete values
  Described by difference equations (Example: queuing systems)

## Slide 2: Definition of Simulation
Simulation is the study of a process through observation of the behavior of a model over time in response to a pattern of inputs.

## Slide 3: Definition of Simulation Model
Un modello di simulazione è uno strumento in grado di elaborare informazioni e dati disponibili per aggiungerne di nuovi a quelli esistenti e di prevedere le risposte di un sistema reale a determinati input divenendo così un efficace supporto in processi di analisi, valutazione di performance e decisione.

## Slide 4: Use of Simulation
Il suo utilizzo è indicato in tutte quelle situazioni in cui le sperimentazioni su sistemi reali, o non ancora esistenti, possono essere distruttive, non costo-efficaci o impossibili

## Slide 5: Goals of Simulation
Determine reliable delivery time
Identify any bottlenecks
Evaluate alternatives to reduce lead time
Identify and reduce possible risks

## Slide 6: Simulation Development Overview

## Slide 7: Simulation Project
OBIETTIVO: STUDIO DI OBIETTIVI REALIZZABILI NEL MONDO REALE (NON LA MODELLAZIONE IN SE)
Consiste in ESPERIMENTI (differenze nella logica o nei dati del modello)
ESPERIMENTO: consiste in REPLICAZIONI (stessa logica ma con la generazione di un insieme diverso di numeri casuali)
RUN: fase tra l’avvio e l’arresto della singola replicazione

## Slide 8: Criteri di progettazione
MODULARITA’
L’intero sistema è scomponibile in più parti
distinte e distinguibili rappresentative di specifiche funzioni
FLESSIBILITA’
Capacità di modificare agevolmente parametri e blocchi logici che condizionano il funzionamento del modello.
INTEGRABILITA’
Scambio automatico dei dati con altri applicativi

## Slide 9: Our Approach
DEFINIZIONE DEL SISTEMA
ACQUISIZIONE ED ANALISI DATI
COSTRUZIONE, VERIFICA DEL MODELLO CONCETTUALE
COSTRUZIONE DEL MODELLO DI SIMULAZIONE
VERIFICA
VALIDAZIONE
SPERIMENTAZIONE
ANALISI DEI RISULTATI
DOCUMENTAZIONE E PRESENTAZIONE RISULTATI
IMPLEMENTAZIONE SUL SISTEMA REALE

## Slide 10: Verification
Verification is the determination that the model and simulation are operating in the manner intended - that the logic of the simulation program is correct and is correctly implemented.
Il processo di determinazione che l’implementazione del modello rappresenta accuratamente la descrizione concettuale e le specifiche dello sviluppatore. Viene svolta continuamente durante lo sviluppo.

## Slide 11: Validation of Simulation
Validation is the determination that the simulated system closely approximates the real system for the given scope.
Il processo di determinazione del grado con cui un modello è una accurata rappresentazione del mondo reale concordemente con gli obiettivi e per gli usi con cui è stato progettato.

## Slide 12: Simulazione: supporto
SUPPORTO PER DIVERSI APPROCCI AL CAMBIAMENTO:
TQM (manufacturing-oriented): flussi fisici
JIT (manufacturing-oriented): flussi fisici
BPR: flussi informativi predominanti/flussi fisici
PROCESS INNOVATION: flussi informativi
KNOWLEDGE MANAGEMENT: flussi informativi

## Slide 13: Vantaggi
Sono possibili indagini che non causano perturbazioni ai sistemi esistenti
Incremento di comprensione del sistema
Cattura di fenomeni aleatori che incidono sulle prestazioni
Espansione/Compressione del tempo simulato
Sono spesso più convincenti e più comprensibili rispetto le formulazioni matematiche

## Slide 14: Punti critici
Specifico apprendimento di tecniche e strumenti (tempo apprendimento e sviluppo)
Assunzioni critiche: scostamento insoddisfacente dalla realtà
Problemi di interpretazione di risultati e loro correttezza
Livello di dettaglio eccessivo
Documentazione carente
Strumenti inadatti

## Slide 15: Basic Model Structure

## Slide 16: Entities
Objects of interest, processed by the model
  e.g. customers, data packets, forms, products, ...
Entities have attributes - can affect routing
  e.g. size, color, quantity
Arrival times collected during modeling
Often aggregated or transformed
  e.g. components-to-product
  EXTERNAL ENTITIES: sviluppatore
  INTERNAL ENTITIES: software

## Slide 17: Attributes
Attributes are properties of entities
  significant for simulation
    arrival rates & distributions, sizes, colors, etc.
  can affect service times & distributions
  can affect direction of entity flow
  can have logical values (active, inactive, etc.)

## Slide 18: Arrivals
Entry of an entity into process domain
  Periodic (repetitive at time interval)
    e.g. sampling every 100th entity for Q.C.
  Scheduled (one-time)
  Randomly distributed
    interarrival time governed by distribution function
    quantity governed by distribution function
  Triggered by event
    level, logical condition, etc

## Slide 19: Activities/Operations
Functions performed by queue servers
  Use time or create events
  Define what happens to entities in time interval
  Associated with process elements
May depend upon attributes of entities
  e.g. grocery line checkout (quantity attribute)
  e.g. airline ticket class (Q.O.S. attribute)

## Slide 20: Resources
Auxiliary personnel or material used to process entities
  Have downtime
    scheduled (deterministic)
    unscheduled (statistical)
  Can be depleted and require renewal/recycling
  Can be of triggering type (Kanban cards)
  Can have parameters (rates of delivery, sizes,...)

## Slide 21: Downtimes and Risk Reduction
Reducing MTTR reduces loss due to outage time
MTBF = Mean Time Between Failure
MTTR = Mean Time to Repair

## Slide 22: Paths
Routes taken by entities in a system
  determined (fixed)
  random (probability distribution)
  dependent (capacity limit, failure event)
Have attributes (speed, capacity, etc.)
Can be disabled due to failure
Cause entity transit time delay

## Slide 23: Transit Time Delay
Depends on path length
Depends on rate of movement
Time = Distance/Rate

## Slide 24: State
Collection of variables needed to describe the system - predict its behavior in the future in response to input (what you would need to save to resume after stopping)
number of busy tellers, number of queued customers, number of customers being served, etc.

## Slide 25: Event
An instantaneous occurrence that can alter the state of the system
Two types:
  exogenous - activities external to the system endogenous - activities internal to the system e.g. completion of service

## Slide 26: Components
Constituent parts of a system
  e.g. elements, subsystems, etc.
Can be process elements or subsystems
  process elements require models
  subsystems require expansion to the level of process elements before models can be entered

## Slide 27: Parameters
Quantities that can take on arbitrary values, to be assigned by the operator of the model
  e.g. arrival rates, maximum queue length, service times
Remain constant for duration of simulation
  e.g. arrival models and statistical parameters
  e.g. service times or rates and model parameters

## Slide 28: Variables
Quantities that can assume only those values permitted by the form of the model
  e.g. length of queue, number of customers being served, etc.
Independent - input variables
  subject to their source models
Dependent - process variables
  subject to laws of process models

## Slide 29: Functional Properties
Mathematical description of the physical behavior of the dependent variables (outputs) for the given parameters, initial state, and inputs (independent variables).
  Server modeled by exponential service time distribution
  e.g. flow splitting, batching, assembly, etc.

## Slide 30: Constraints
Limitations placed upon the permitted values of variables or upon the allocation of resources
  e.g. maximum queue length, maximum number of servers
  e.g. minimum interarrival time

## Slide 31: Basics of Queuing Systems
An introduction to the statistics of queuing systems.

## Slide 32: Basic Queuing Model
M/M/1 Queue

## Slide 33: Notation
M/M/1 1= number of servers M=Service: M=exponential G=general D=deterministic (constant)
M= Arrivals: Poisson (Markov) process

## Slide 34: Server
Removes item from queue for service, when server is not busy
Service time is statistical
  depends upon server
  depends upon length of service required
  server is busy until service complete (service completion event)
Multiple servers are possible

## Slide 35: Multiple-Server Queue

## Slide 36: Examples
Print spooler (single queue and server)
Post office (single queue, multiple servers)
Airline ticket lines (multiple queues, multiple servers on some queues)

## Slide 37: Queuing Analysis

## Slide 38: Hierarchic Simulation Modeling
Top-down model layout
  start with highest layer (main operations)
  define these in terms of sub-operations
  insert activity models in lowest layer
Show names of operations at each layer
Show entity names at each layer

## Slide 39: Elements of a Process Model
Arrival process (statistical)
Service process (statistical)
Path considerations
Resources used
Costs

## Slide 40: Arrival Data
Entity name
Quantity
Time stamp
  Date
  Time
  Location
Attribute(s)

## Slide 41: Arrivals with Time Stamp
Arrival times and interarrival intervals for car wash – field data.

## Slide 42: Path Data
Length of path
Travel velocity or time
Attribute dependencies
Interferences
  regular (drawbridge openings)
  statistical (warehouse fork lifts)

## Slide 43: Queue Data
Number of queues
Length(s)
Discipline(s)
  FIFO
  Priority
  Other

## Slide 44: Service Data
Number of servers
Server properties
  Service time
  Quality of server
  Resources used (types)
  Resource downtimes expected
  Costs
Processes performed

## Slide 45: Exit Data
Entity name
Quantity
Time stamp
  Date
  Time
  Location

## Slide 46: Simulation Studies
Set objective
Build model to serve objective
Capture data appropriate to objective
Analyze with respect to objective

## Slide 47: Simulation Studies
Process development: robustness/limitations of the system
Process optimization: optimize system performance - minimize operating costs
Process alternatives: process improvements, sensitivity analysis, reduction resource related processing costs, delays, inventory

## Slide 48: Process Development

## Slide 49: Process Development
Model fixed (selection)
Parameters fixed (best fit to data)
Inputs varied (to change outputs)
Outputs varied (get desired results)
Robustness/limitations of the system

## Slide 50: Process Optimization

## Slide 51: Process Optimization
Inputs fixed (field data)
Model fixed (selection)
Parameters varied (optimize outputs)
Outputs varied (to produce best results)
Optimize system performance - minimize operating costs

## Slide 52: Optimization (Operations)
Fixed model and input data
Adjust some parameters
Review simulation results
Repeat parameter adjustment to optimize

## Slide 53: Process Alternatives

## Slide 54: Process Alternatives
Inputs fixed (field data)
Model varied (for best results)
Parameters varied (for best model)
Outputs varied (best results)
Process improvements, sensitivity analysis, reduction resource related processing costs, delays, inventory

## Slide 55: Implications (Problem Formulation)
What is the process?
  What aspect is to be simulated?
  What laws govern its behavior?
What form should simulation take?
  Discrete?
  Continuous?

## Slide 56: Related Issues
user interface
data capture interface
data storage (often large files)
fitting of distributions & models
data presentation
programming requirements

## Slide 57: Implications (Study Objectives)
What should be the result?
What will be the expected benefits?
Who will be the users of the results?

## Slide 58: Implications (Model)
What natural laws are represented?
What assumptions, goals, measures?
What boundary (limiting) conditions?
What form (package, language)?
How is it to be validated?

## Slide 59: Implications (Data Collection)
What data (how much, what type)?
How often?
How executed?
What conditions?
How processed?
What precision?
What format?

## Slide 60: Implications (Coding)
Package or language?
What speed desired?
Graphical effects?
Object oriented?
What interfaces?

## Slide 61: Implications (Verification)
How will this be accomplished?
Testing of random number generator?
Testing of time function inputs?
Testing of traffic generation model?
Review of data gathered (observations)?
Check physical units?
Verification of predicted values?

## Slide 62: Implications (Experimental Design)
For observability
To validate the model
To validate the simulation

## Slide 63: Implications (Analysis of Results)
Do results make sense?
Is time/physical scale (detail) appropriate?
What inferences can be drawn?
Are further studies needed?

## Slide 64: Implications (Documentation)
How will models be documented?
How will results be presented?
Save all for further studies?